## Slide 1
Final Demo Day

## Slide 2: Member: Gen, Li, Technical University of Munich Team - SoloGen

## Slide 3: Advanced Energy Management System for Utility-Scale Battery Storage
Team SoloGen

## Slide 4: Develop an intelligent EMS for a 4.5 MWh BESS to maximize profitability across European electricity markets while managing battery degradation OBJECTIVE

## Slide 5: 1. Model and Implementation: 2. Results and Performance: 3. Business Impact: 4. Discussion, Outlook and Conclusion: AGENDA

## Slide 6: 1. Four-market optimization - Day-ahead energy - FCR capacity - aFRR capacity - aFRR energy 2. Battery degradation modeling - Cyclic aging costs - Calendar aging costs 3. 10-year investment analysis Phase II Deliveries
Battery Specifications
- Capacity: 4,472 kWh
- Efficiency: 95% round-trip
- C-rates: 0.25, 0.33, 0.50
- Daily cycles: 1.0, 1.5, 2.0

## Slide 7: Model and Implementation Three-Stage Model Architecture
Model I: Phase I Model + aFRR Energy
s.t.
BESS Physical Rules
Market Rules
Energy Balance
BESS Physical Rules
Market Rules
Energy Balance
Model III: Model II + Calendar Aging
s.t.
Model II constraints
Calender Aging Constraints
Model II: Model I + Cyclic Aging
s.t.
Model I constraints
Cyclic Aging Constraints

## Slide 8: Model and Implementation Three-Stage Model Architecture
Model I: Phase I Model + aFRR Energy
Model Components:
(CST-2) SOC Limits
(CST-3) Prevent Simultaneous Operation
(CST-5) Market Co-optimization Power Limits
(CST-4) Ancillary Service Energy Reserve
(CST-6) Cross-Markets Mutual Exclusivity
(CST-1) SOC Dynamics (Energy Balance)
(CST-7) Daily Cycle Limits
(CST-8) Max/Min Bounds
Objective Function
Components

## Slide 9: Model and Implementation Three-Stage Model Architecture
Model I: Phase I Model + aFRR Energy
s.t.
BESS Physical Rules
Market Rules
Energy Balance
BESS Physical Rules
Market Rules
Energy Balance
Model II: Model I + Cyclic Aging

## Slide 10: Model and Implementation Three-Stage Model Architecture
BESS Physical Rules
Market Rules
Energy Balance
Model II: Model I + Cyclic Aging
(CST-ii-1) Degradation-Aware SOC Dynamics
(CST-ii-2) SOC & Segment Limits
(CST-ii-3)
Require BESS energy is stored sequentially
(CST-ii-4)
Require BESS energy (dis-)charge sequentially to BESS segments.
(CST-ii-1) Cyclic Aging Cost
(CST-ii-5) Min/Max Bounds

## Slide 11: Model and Implementation Three-Stage Model Architecture
BESS Physical Rules
Market Rules
Energy Balance
Model III: Model II + Calendar Aging
s.t.
Model II constraints
Calender Aging Constraints
Model II: Model I + Cyclic Aging
s.t.
Model I constraints
Cyclic Aging Constraints

## Slide 12: Model and Implementation Three-Stage Model Architecture
Model III: Model II + Calendar Aging
Model Components:
Calendar Aging Cost
(CST-7) Calendar Aging PWL Constraints

## Slide 13: Model and Implementation MPC Framework Architecture

## Slide 14
Results and Performance Optimizer Case Study: CZ
Technical Achivements ⚙️
✅ Three-layer optimization architecture
✅ Cyclic Aging enforcement (Xu 2017)
✅ SOS2 calendar aging (Collath 2023)
✅ Production MPC with checkpointing
✅ 100% scenario completion rate

## Slide 15
Results and Performance MPC Total Profit Analysis
Strategic Investment Recommendations
1. Priority Markets
- 🇨🇭 Switzerland: Highest absolute returns
- 🇨🇿 Czech Republic: Strong risk-adjusted returns
2. Configuration Strategy
- Always select C-rate 0.50
- Optimize daily cycles via MPC
3. Risk Considerations
- Market saturation in Germany
- Regulatory changes in CEE markets

## Slide 16
Results and Performance MPC Total Profit Analysis
Strategic Investment Recommendations
1. Priority Markets
- 🇨🇭 Switzerland: Highest absolute returns
- 🇨🇿 Czech Republic: Strong risk-adjusted returns
2. Configuration Strategy
- Always select C-rate 0.50
- Optimize daily cycles via MPC
3. Risk Considerations
- Market saturation in Germany
- Regulatory changes in CEE markets

## Slide 17
Results and Performance Optimizer Case Study: CZ – May 12th 2024
The SOC check of three models

## Slide 18
Results and Performance Optimizer Case Study: CZ – May 12th
Solver: Gurobi 13.0.0
Hardware: Intel i9-12900K (16 cores, 24 threads) | RAM: 64 GB

## Slide 19
Results and Performance Optimizer Case Study: CZ

## Slide 20: We delivered a BESS optimizer that: Conclusion
Maximizes profitability across four European electricity markets
Manages degradation through advanced aging models
Scales efficiently to full-year horizons Provides actionable insights for investment decisions
Ready for Deployment
Professional codebase with comprehensive documentation @ https://github.com/GenLI3202/TechArena2025_EMS
Extensible architecture for future enhancements

## Slide 21
Thank You
Contact:
gen.li@tum.de